## Slide 1: Specimen Collection
April 2022
Clair Stokes
Infection Prevention and Control

## Slide 2: Introduction Specimen containers an transport bags Microbiology specimen collection Storage Labelling Spillages of specimens

## Slide 3: Introduction
A specimen is a sample of body fluid, e.g. urine, faeces. All specimens are a potential infection risk, therefore all specimens must be collected using standard precautions. Specimens should be transported in a ridged container in accordance with the Carriage of Dangerous goods and Use of Transportable Pressure Equipment (2009)
Taking routine specimens should be avoided to help reduce inappropriate prescribing of antibiotic treatment. Specimens should only be taken if there are indications of clinical infection.
Urine should not be dipsticked for nitrates and leukocytes unless there are clinical signs of a urinary tract infection, treating a positive dipstick for nitrates and leukocytes without clinical signs of an infection may result in inappropriate prescribing of antibiotics.

## Slide 4: Specimen containers and transport bags
The person who obtains the specimen should ensure:
The container is appropriate for the purpose and is CE marked. If there is leakage or an inappropriate container is used, the specimen will not be processed by the lab due to the infection risk.
The lid is securely closed
There is no external contamination of the outer container by the contents
Specimens are placed inside the plastic transport bag attached to the request form after they have been labeled
The transport bag should be sealed using the integral sealing strip (not stapled)
For large specimens e.g 24 hour urine collections may be enclosed in a clear plastic bag tied at the neck. The request for should also be tied at the neck of the bag.
Specimens received from residents/ service users should be transported to GP surgeries in a wipable ridged container.

## Slide 5: Microbiology Specimen Collection
Sample | Key Information | Indication | Container
Faeces | Open bowel into a receptacle, e.g. commode. Scoop a sample of faeces into the specimen container using the container spoon provided. NB: Faecal specimens can be taken even if contaminated with urine. | Diarrhoea, increase in frequency, presence of blood, abdominal pain | Stool Specimen container (at least ¼ full)
Nasal Swabs | Gently rotate the swab ensuring it is touching the inside of the nostril. Repeat the process using the same swab for the other nostril | Provide a COVID swab or MRSA swab | Sterile cotton swab in provided container.
Sputum | Sputum should be expectorated directly into a sterile container. Early morning specimens taken before eating provide the best results. | Productive cough( green or yellow) or presence of blood in sputum | Plain universal container
Urine midstream (male) | Retract the foreskin and clean the surrounding the surrounding urethral meatus with soap and water. Urinate first part into the toilet, collecting the middle part of the specimen into a sterile bowl. Pass the remainder into the toilet. Replace the foreskin | Pain on passing urine, increase in frequency, fever, new incontinence, new or worsening confusion, flank or low abdominal pain | Universal container with boric acid preservative (red top) which prevents bacteria from multiplying in the container. If sample is less than 5ml, a white top container must be used as the preservative in the red topped bottle will be too potent and may kill off any organisms.
Urine midstream (female) | Clean the genitalia with soap and warm water, wiping from front to back. Urinate, first part into the toilet, collecting the middle part of the flow into a sterile container. Pass the remainder into the toilet | Pain on passing urine, increase in frequency, fever, new incontinence, new or worsening confusion, flank or low abdominal pain | Universal container with boric acid preservative (red top) which prevents bacteria from multiplying in the container. If sample is less than 5ml, a white top container must be used as the preservative in the red topped bottle will be too potent and may kill off any organisms.

## Slide 6: Urine: Catheter specimen of urine
A routine catheter specimen of urine (CSU) is not necessary from catheterised residents/ service users. A specimen should only be obtained:
If there is a clinical indication for treatment (symptoms of a CAUTI) – difficulty in passing urine, need to pass urine urgently and frequently, incontinence, visible blood, shivering, chills or a temperature, confusion and pain in groin or side.
Following catheterisation for retention.

## Slide 7: Collecting a CSU
Samples must be obtained from the self-sealing sampling port of the drainage tubing, not from the drainage bag. Never collect a sample of urine from the drainage bag as tis does not represent the bacteria in the bladder and could lead to over prescribing of antibiotics.
Never disconnect the closed system to obtain a urine sample.
Wash and Dry hands, wear disposable apron and gloves, clean the sampling port with 70% isopropyl alcohol and allow to dry. Use a sterile syringe to access the sampling port and obtain a specimen.
Transfer the specimen into a sterile 30ml universal container with boric acid preservative (red top) which prevents bacteria from multiplying in the container. If sample is less than 5ml, a white top universal container must be used as the preservative in the red topped bottle will be too potent and may kill off any organisms.
The specimen must be sent to the laboratory as soon as possible or refrigerate at 4˚C until collection, which must be within 24hrs.
Wipe the sampling port again with 70% isopropyl alcohol.
Dispose of the empty syringe as infectious waste.
Remove personal protective equipment and wash hands.
Complete the specimen request form, including details of the type of specimen, clinical details, any antibiotic treatment and symptoms.

## Slide 8: Storage
Wherever possible, obtain a fresh specimen and take the specimen at a time when it can be transported to the GP practice in a timely manner.
For the most accurate results, specimens should be received by the laboratory as soon as possible or at least within 24 hrs. After this time, any dominant or more virulent micro-organisms will flourish and weaker ones will die off, which can lead to inaccurate results.
If delivery is delayed, the specimen should be placed ideally in a ‘specimen’ designated fridge.
Regular cleaning of specimen refrigerator and temperature should be documented.

## Slide 9: Labelling
Specimens must be labelled correctly to prevent misdiagnosis and waste. The specimen request form and the specimen container label must be completely filled in.
All specimens must be clearly labelled with the correct resident’s details which include:
Residents full name
Residents address
Male or Female
Date of Birth and NHS Number
Type of specimen (CSU or midstream urine)
Relevant clinical details, symptoms and duration etc.
Medical history if relevant i.e. antibiotics
If viral diarrhoea outbreak add iLog number of outbreak from PHe
Date and time of collection of specimen
Signature
GP and Practice details
Hazardous groups if any i.e. TB (Danger of Infection)

## Slide 10: Spillages of specimens
Spillages of blood or body fluids should be dealt with immediately and in accordance with standard precautions.
Should the container leak, a new specimen should be obtained. If this is not possible, carefully decant the specimen into a clean container whilst wearing appropriate PPE (personal protective equipment).
If the outside of the container is contaminated, it should be disinfected with an appropriate wipe. If the specimen form is contaminated, a new form should be used.

## Slide 11: References
Harrogate and District NHS Foundation Trust – Specimen Collection
Department of Health (2007) Transport of Infectious Substances – Best Practice guidance for microbiology laboratories.
Health and Safety (2009) Carriage of Dangerous Goods and Use of Transportable Pressure Equipment
Royal Marsden NHS Foundation Trust (2015) The Royal Marsden Hospital Manual of Clinical Nursing Procedures 9th Edition